## Slide 1: 4x7 600W Standard PSU Design Proposal
Andrew Mosqueda

## Slide 2: Small 600W 1U Competitors (Fan installed)
Competitor | up specs | down specs | Common Specs
TDK CUS600M 3.35x6.18x1.67 | Smallest Size - 3.35x6.18 Has 19V, 28V, 32V, 36V variants Highest efficiency 96%@0.5load (vs 94%) | Narrow output voltage adjust range - 7.5% Max temp non-derated - 45℃(vs50℃) Min voltage input non-derated - 115V (vs90Vac) Latch on power output short circuit (vs hiccup) Overtemp latch vs (autorecover) No Stdby ovp sense (vs latch including power) Audible noise not provided (vs 38dB) Fan connected across 5V, no PWM (vs 12V PWM) No Parallel Sharing (vs active sharing x2 PSU) No PMBus Lowest Holdup 14ms (vs 17artesyn, 20Delta) | 12V, 24V and 48V variants 0W minimum load Power output overcurrent shutdown and auto recover Power output overvoltage latch Remote On/Off (PSON) 5V standby output Standby OCP hiccup - main output also shutdowns. Vin Input Frequency 47-63Hz Safety IEC60601-1 3rd, IEC62368-1 approvals Emmision/Immunity IEC61000-3-2 Class A, EN55032/EN55011-B, EN60601-1-2:2015 approvals Vibration/Shock IEC60068-2 approvals Pollution Degree 2
DELTA IMA-X600 4x8x1.6 | Wide output voltage adjust range - +/-20% With LED green indicator Lowest Inrush 20Apk (vs 50Apk) | Largest size - 4x8 No convection cooled option (vs 400W) No power off consumption specified | 
ARTESYN CNS650 4x7x1.57 | Power output constant current, Reduce Vo down to 50% before hiccup. High output remote sense compensation 1.8V (vs 0.5V) Separate Vin/Po Good pins. Can operate at 360-440Hz Input Frequency with higher leakage (inherent due to EMI Y-caps). Lowest power off consumption 0.5W (TDK 0.5W + 2.5W fan) Fan PWM override pin. Fan fault pin. | Output voltage can't be adjusted lower, only higher up to 15% | 

## Slide 3: Design Proposal
Follow common Specs of the three power supplies (4th column of the table on the previous slide)
Compete with the best specs competitor (Artesyn CNS650) but with better specs:
Specs | Value | Difference
Size | 4x7x1U | Same
Output Variants | 12,24,36,48 | Fill 36V gap. Use for 36V motors and batteries.
Output Adjust Range | +/-20% | Competitor cannot reduce output voltage. Only increase.
Max Parallel | 4 (also A0, A1 for address pin instead of only A0). | Competitor can only parallel 2 units.
Constant Current | Yes | Same (A challenge)
ARTESYN CNS650 PSU Specs Attached:

## Slide 4: PFC Topology
Strategy | Why
Follow TDK Lambda PSU Conventional Single Choke DCM-CCM Topology | Minimize component count and BOM cost
Use UCC28180 (same as used by TDK Lambda Controller ) as close loop controller. | Minimize time to market. (Part available in iPower)
Add cheap microcontroller IC | For metering

## Slide 5: DC-DC Topology
Strategy | Why | Risk-Solution
Use Half-Bridge LLC | Minimize component count and BOM cost | LLC output voltage range is limited - Vref info is feed back to PFC to reduce/increase the DC bus during VR adjustment. - Vref info is used to control the LLC controller to enable burst during constant current. (Check IC if capable) -Reverse engineer the Artesyn PSU schematic.
Use analog controller similar with TDK lambda. HR1001A | The part L6599AD controller that is being used by TDK lambda is not available in iPower. HR1001A is used in several models. | 
Add microcontroller IC | PMbus, Housekeeping. | 

## Slide 6: HR1001 Usage
PA-1501-1L, PA-2261-6L1, PA-2311-15, PA-2401-20GR, PA-2501-3P, PS-2251-3S, PS-2302-9A, PS-2401-3S1, PS-2601-3S

## Slide 7: Activities
Acquire TDK-Lambda and Artesyn PSU.
Electrical Specs Characterization of competitor PSU and also Thermal. (2 weeks)
Reverse engineer the circuit of TDK-Lambda and Artesyn PSU. (1 wk each PSU)
Magnetics Characterization (2 weeks)
Schematic Generation (2 weeks)
Calculation (2 weeks)
BOM Generation (2 weeks)

## Slide 8: L6599A Usage
None